Combinational Logic Design Review
COE203
Digital Logic Laboratory
Dr. Ahmad Almulhem
COE - KFUPM
Spring 2009

---
Combinational Circuits
Combinational
Circuits
Input
X
Output
Z
.
.
.
.
Z = F(X)
In combinational circuits, the output at any time is a direct function of the applied external inputs

---
Design procedure
Circuit Specification
Truth Table
How many input/output?
Minimization
K-maps, Algebraic Manipulation. Computer based tools
Logic Diagram

---
Example
Design a combinational circuit which has 3-bit input number and a single output F where:
- F = 1 when the input number is less than 3
- F = 0 otherwise.

---
Design with MSI
- Decoder (n → 2n)
  - Example 2-to-4 decoder
- Encoder (2n → n)
  - Example: 8-to-3 encoder
- Multiplexer (n → 1)
- Demultiplexer (1 → n)
- Comparator (=, <, >)

---
Question
A majority function has an output of 1 if there are more 1’s than 0’s in the inputs. Design a 3-input majority function.
1. Fill the truth table.
2. Use K-map to simplify F
3. Draw the circuit

---
Assignment
Review Chp 6 & Chp 7 for next time