Exp#3
Introduction To FPGA
Design Flow
COE203
Digital Logic Laboratory
Dr. Ahmad Almulhem
COE - KFUPM
Spring 2009

---
What is an FPGA?
Configurable
Logic
Blocks
I/O
Blocks
Block
RAMs
A filed programmable gate array (FPGA) is a programmable
integrated circuit (IC)
Block RAMs
Block RAMs

---
CLB Slice Structure
- Each slice contains two sets of the following:
  - Four-input LUT
    - Any 4-input logic function,
    - or 16-bit x 1 sync RAM
    - or 16-bit shift register
  - Carry & Control
    - Fast arithmetic logic
    - Multiplier logic
    - Multiplexer logic
  - Storage element
    - Latch or flip-flop
    - Set and reset
    - True or inverted inputs
    - Sync. or async. control

---
LUT (Look-Up Table) Functionality
- Look-Up tables are primary elements for logic implementation
- Each LUT can implement any function of 4 inputs

---
Routing Resources
PSM
PSM
CLB
PSM
PSM
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
Programmable
Switch
Matrix

---
FPGA Design Flow
design
bitstream
00101...

---
Xilinx ISE 7.1i

---
Digilent Spartan-3 Board
- 200K gate Xilinx Spartan-3 FPGA
- 8 slide switches
- 4 pushbuttons
- 8 LEDs
- 4-digit seven-segment display
- Serial port
- VGA port
- PS/2
- And others ....

---
FPGA Device Marking
We are using Spartan 3 XC3S200-ft256

---
Today's Lab
- Tasks:
  - Get familiar with Digilent Boad
  - Get familiar with Xilinx ISE tools
  - Build full-adder (Lab 1)
- Need help?
  - Tutorials, documentations
  - Menu → Help (F1)
  - Under resources in the website