Exp#5 & 6
Introduction to Verilog
COE203
Digital Logic Laboratory
Dr. Ahmad Almulhem
KFUPM
Spring 2009

---
What is Verilog?
- Verilog is a hardware description language (HDL)
- Can describe everything from single gate to a compete computer system
- Allows to design at Behavior Level, Register Transfer Level (RTL), Gate level and at switch level
- Syntax is similar to C language (case-sensitize, similar keywords)
- Parallel not serial (Not like C language)
- Technology-independent, easy to design and debug
- Most popular HDLs are VHDL and Verilog

---
Why use HDL ?
- Digital systems are highly complex; millions of transistors.
- For large digital systems, gate-level design is unmanageable
- HDL offers the mechanism to describe, test and synthesize large designs
- Computer-aided design tools aid in the design process.
- © Intel P4 Processor
- Introduced in 2000
- 40 Million Transistors
- 1.5GHz Clock

---
Levels of description in Verilog
- Switch Level
  - Layout of the wires, resistors and transistors on an Integrated Circuit (IC) chip
- Gate (structural) Level
  - Logical gates, flip flops and their interconnection
- RTL (dataflow) Level
  - The registers and the transfers of vectors of information between registers
- Behavioral (algorithmic) Level
  - Highest level of abstraction
  - Description of algorithm without hardware implementation details (like C programming)

---
Modules in Verilog
- In Verilog, a digital system is described as a set of modules
- Each module has a port list (interface) to other modules
- Modules can represent pieces of hardware ranging from simple gates to complete systems, e. g., a microprocessor.

---
Gate Level (Structural) Modeling
- Text description of the circuit structure (netlist)
  - built-in primitives gates
// my gate
module my_gate(OUT1, IN1, IN2);
     output OUT1;
     input IN1, IN2;
     wire X;
     and (X, IN1, IN2);
     not (OUT1, X);
endmodule
IN1
OUT1
X
IN2
Any internal net must be defined as wire
Internal Signal

---
Verilog Primitives
Basic logic gates only
- and
- or
- not
- buf
- xor
- nand
- nor
- xnor
- bufif1, bufif0
- notif1, notif0

---
Primitive Pins Are Expandable
nand (y, in1, in2) ;
nand (y, in1, in2, in3) ;
nand (y, in1, in2, in3, in4) ;

---
A Half Adder
// Half Adder
module hadd (S, C, X, Y);
input X, Y;
output S, C;
xor (S, X, Y);
and (C, X, Y);
endmodule

---
Instantiation of Modules
// Full Adder
module fadd (S, C, X, Y, Z);
input X, Y, Z;
output S, C;
wire w1, w2, w3;
hadd M1 (w1, w2, X, Y);
hadd M2 (S, w3, w1, Z);
or (C, w2, w3);
endmodule
w1
w2
w3
- Here we instantiate hadd twice. i.e., placing two hadd circuits and connecting them.
- This full adder is built from two half adders and an OR gate.

---
3-bit Adder
module add3 (s,cout,ci,a,b);
input [2:0] a,b; // port declarations
input ci ;
output [2:0] s;	// vector
output cout;
wire [1:0] co;
fadd a0 (co[0], s[0], a[0], b[0], ci);
fadd a1 (co[1], s[1], a[1], b[1], co[0]);
fadd a2 (co[2], s[2], a[2], b[2], co[1]);
endmodule
a[2] b[2]
a[1] b[1]
a[0] b[0]
a2
a1
a0
cout
ci
co[1]
co[0]
s[2]
s[1]
s[0]

---
Continuous Assignments
- Describe combinational logic
- Operands + operators
- Drive values to a net
  - assign out = a&b ;	// and gate
  - assign eq = (a==b) ;	// comparator
- Changes to right hand side are evaluated and the result propagated to the left hand side
- Avoid logic loops
  - assign a = b + a ;

---
Simple XOR Gate
// simple xor gate using RTL
module my_xor( C, A, B );
   output C;
   input A, B;
   assign C = (A ^ B);
endmodule
Operation Operator
       ~ Bitwise NOT
       & Bitwise AND
        | Bitwise OR
       ^ Bitwise XOR

---
Full Adder
module fadd (S, Cout, A, B, Cin);
    output S, Cout;
    input A, B, Cin;
    assign S = A ^ (B ^ Cin);
    assign Cout = (A & B)|(A & Cin)|(B & Cin);
endmodule
Can we change the order of the assign statements?

---
Behavioral Description of an Adder
module adder3 (S, Cout, A, B, Cin);
   input [2:0] A, B;
   input Cin;
   output [2:0] S;
   output Cout;
   assign { Cout, S } = A + B + Cin;
// note: Verilog treats wires
  // as ‘unsigned’ numbers
endmodule
3-bit operands,
4-bit result
 { Cout, S } is a 5 bit bus:
 Cout S[3] S[2] S[1] S[0]

---
Behavioral Description of an Adder
module adder (S, Cout, A, B, Cin);
   parameter	width = 2;
   input Cin;
   input [width:0] A, B;
   output [width:0] S;
   output Cout;
   assign { Cout, S } = A + B + Cin;
endmodule

---
Logic Values
The underlying data representation allows for any bit to have one of four values
- 0: for "logic 0” ,or a false condition
- 1: for "logic 1", or a true condition
- z: for the high-impedance state
- x: for an unknown value

---
Data Types
Net: wire
- variables represent physical connections between structural entities such as gates.
- A wire does not store a value.
Registers: reg
store the last value that was procedurally assigned to them

---
Number representation
- Format: <size><base format><number>
  - <size>: number of bits (optional)
  - <base format>: 'b, 'd, 'o, 'h
  - <number>: digits which are legal for the <base format>
- Examples:
  - 549	// decimal number
  - 'h 8FF	// hex number
  - 'o765	// octal number
  - 4'b11	// 4-bit binary number 0011
  - 3'b10x	// 3-bit binary number with least significant bit unknown
  - 5'd3	// 5-bit decimal number
  - -4'b11	// 4-bit two's complement of 0011, or equivalently 1101

---
Operators
{ }	concatenation
+ - * /
arithmetic
%	modulus
> >= < <=
relational
!	logical NOT
&&	logical AND
||	logical OR
==	logical equality
!=	logical inequality
? :	conditional
~	bit-wise NOT
&	bit-wise AND
|	bit-wise OR
^	bit-wise XOR
^~ ~^	bit-wise XNOR
&	reduction AND
|	reduction OR
~&	reduction NAND
~|	reduction NOR
^	reduction XOR
~^ ^~	reduction XNOR
<<	shift left
>>	shift right

---
Always Block
always @(sensitivity_list)
   begin [optional name]
    [optional local declaration];
    [procedural statement];
    [procedural statement];
    .....
   end
- always blocks are procedural blocks that contain sequential statements (order is important).
- It executes when sensitivity_list changes:
  - Level change: always @(a or b or c)
  - Edge change: always @(posedge clock)
  - Edge change: always @(negedge clock)
- if-else and case statement are only in always block

---
Wire vs. Reg
There are two types of variables in Verilog:
- Wires (all outputs of assign statements must be wires)
- Regs (all outputs of always blocks must be regs)
Both variables can be used as inputs anywhere
- Can use regs or wires as inputs (RHS) to assign statements
- assign bus = LatchOutput + ImmediateValue
  // bus must be a wire, but LatchOutput can be a reg
- Can use regs or wires as inputs (RHS) in always blocks
- always @ (in or clk)
     if (clk) out = in  // in can be a wire, out must be a reg

---
Always vs. Assign
module and3(a, b, c, y);
  input wire a, b, c;
  output reg y;
  always @ (a or b or c)
     begin
        y = a;
        y = y & b ;
        y = y & c ;
     end
endmodule
module and3(a, b, c, y);
  input wire a, b, c;
  output wire y;
  assign y = a;
  assign y = y & b ;
  assign y = y & c ;
endmodule

---
If Statements
Syntax:
  if (boolean expression)
  begin
        statements...
  end
  else if (boolean expression)
  begin
        statements...
  end
  else
   begin
        statements...
  end
begin-end can be omitted if only one statement.
Example:

---
Case Statements
Syntax
case (expression)
  case_choice1:
  begin
    ...statements...
  end
  case_choice2:
  begin
    ...statements...
  end
  default:
  begin
    ...statements...
  end
endcase
begin-end can be omitted if only one statement.
Example:

---
If Statements
if (m==n)
   r = a + b + c ;
else if (m > n )
   r = a - b ;
else
   r = c + 1 :
Priority routing network
sequence of 2-to-1 MUX

---
Case Statements
wire [1:0] sel;
case (sel)
   2'bOO: r = a + b + c ;
   2'b1O: r = a - b;
   default : r = c + 1;
endcase
multiplexing network
sequence of n-to-1 MUX

---
Example: Full Adder
module fadd (A, B, Cin, S, Cout);
input A, B, Cin;
output S, Cout;
reg S, Cout;
always @(A or B or Cin)
begin
S = (A ^ B ^ Cin);
Cout = (A & B)|(A&Cin)|(B&Cin);
end
endmodule

---
Example: 2x1 Multiplexer
Method 1
module mux2x1 ( b, c, select, a);
input	b, c, select;
output	a;
assign a = (select ? b : c);
endmodule
Method 3
module mux2x1 ( b, c, select, a);
     input	b, c, select;
     output a; reg a;
     always@(select or b or c) begin
case (select)
    1’b1: a=b;
    1’b0: a=c;
endcase
     end
endmodule
Method 2
module mux2x1 ( b, c, select, a);
input	b, c, select;
output a; reg a;
always@(select or b or c) begin
   if (select) a=b;
   else a=c;
end
endmodule

---
A 2-Bit ALU
module alu (A, B, Y, Sel);
parameter width=2;
input [width-1:0] A, B;
input [2:0] Sel;
output [width-1:0] Y;
reg [width-1:0] Y;
always @(A or B or Sel)
begin
case (Sel[2:0])
3'b000 : Y = ... ;	// A and B
3'b001 : Y = ... ;	// A or B
3'b010 : Y = ... ;	// A xor B
3'b011 : Y = ... ;	// 1’s complement of A
3'b100 : Y = ... ;	// A nand B
3'b101 : Y = ... ;	// A nor B
3'b110 : Y = ... ;	// max(A,B)
default : Y = 0;
endcase
end
endmodule