Exp#7 Finite State Machine Design in Verilog
Exp#7
Finite State Machine Design in Verilog
COE203
Digital Logic Laboratory
Dr. Ahmad Almulhem
KFUPM
Spring 2009

---
Sequential Circuits
- Sequential circuits consist of both combinational logic and storage elements.
- Sequential circuits can be
  - Mealy-type: outputs are a combinatorial function of both Current State signals and primary inputs.
  - Moore-type: outputs are a combinatorial function of Current State signals.
Combinational
Logic
FFs
^
Inputs
Outputs
CLK
Current State
Next State

---
Generalized Verilog Mealy Model
reg Y, D, Z;
// register (current state)
always @ (posedge CLK or posedge Reset)
begin
   if (Reset) Y = 0 else Y = D;
end;
// next state logic
always @ (X or Y)
begin
   D = F1(X, Y);
End;
// output logic
always @ (X or Y)
begin
   Z = F2(X, Y);
end;
X
F2
F1
Z
Register
Y
D
CLK
Reset

---
Generalized Verilog Moore Model
reg Y, D, Z;
// register (current state)
always @ (posedge CLK or posedge Reset)
begin
   if (Reset) Y = 0 else Y = D;
end;
// next state logic
always @ (X or Y)
begin
   D = F1(X, Y);
end;
// output logic
always @ (Y)
begin
   Z = F2(Y);
end;
X
F2
F1
Z
Register
Y
D
CLK
Reset

---
2-Way Traffic Controller
2-Way Traffic Controller
N
operation
Traffic	Action
EW only	EW Signal green / NS Signal red
NS only	NS Signal green / EW Signal red
EW & NS	Alternate
No traffic	Previous state
W
E
S

---
Design
Design
Reset
X = 11
X = 10
X = 00
X = 01
X = 00
X = 10
NS (0)
S=01
EW (1)
S=10
X = 11
X = 01
    INPUTS
Sensors X[1:0]
X[0] : car coming on NS
X[1] : car coming on EW
Clock and Reset.
      OUTPUTS
Signals S[1:0]:
S[0] : NS is green
S[1] : EW is green

---
Verilog Design
Verilog Template
module Traffic_Controller (Clock, Reset, X, S);
  input[1:0] X;
  input Clock, Reset;
  output[1:0] S;
  reg currentState, nextState;
  reg[1:0] S;
// register (Current State)
always @( … )
  begin
  end
// next state logic
always @( … )
  begin
  end
// output logic
always @( … )
  begin
  end
endmodule
You need to
debounce the clock!
Hint: Check Lab4