Exp#8
Programmable Sequence Detector
(Data Path and Control Unit)
COE203
Digital Logic Laboratory
Dr. Ahmad Almulhem
KFUPM
Spring 2009

---
Programmable Sequence Detector
- Receives continuous serial input and compares with stored 4-bit number, asserts Match
- User can change stored number (re-programm)
- Inputs: Clock, Reset, Prog, Sin
- Outputs: Match

---
Data-Path/Control Unit
ext. control
signals
DP control
signals
Control
Unit
(CU)‏
Data
Path
(DP)‏
Data
DP status
signals
ext. status
signals

---
Design

---
Design (Data-Path)

---
Design (Control Unit)
Hint: Check Lab7

---
Design (Control Unit)
module controlUnit(clk, reset, countdone, prog, shifta, shiftb, enable3, clr3);
  input clk, reset, countdone, prog;
  output shifta, shiftb, enable3, clr3;
  reg shifta, shiftb, enable3, clr3;
  reg CS, NS;
  parameter s0= 0, s1=1;
// register (Current State)
always @ (posedge clk or posedge reset)
begin:
  ...
end
// next state logic (Transition)
always @ (countdone or prog or CS)
begin: Transitions
 case (CS)
   s0: ....
   s1: ....
   default: ...
 endcase
end
// output logic
always @ (prog or CS)
begin: Output
 case (CS)
   s0: ....
   s1: ...
   default: ...
  endcase
 end

---
Design (Complete)
reset
serial
match
Data Path
shiftA
shiftB
enable3
clr3
countDone
Debounce
Control Unit
prog
reset