Sequential Circuits
COE203
Digital Logic Laboratory
Dr. Ahmad Almulhem
COE - KFUPM
Spring 2009

---
Sequential Circuits
Input
X
Output
Z
Combinational
Circuits
States
Y
Memory
Z = F(X,Y)
- The outputs, Z, depends both on the present inputs, X, and the present state Y.
- The next state depends on the inputs X and the present state Y.

---
Example
- 4-bit adder (ripple-carry)
  - Notice how carry-out propagates
- 4 full adders are needed

---
Example (cont.)
- 1-bit memory and 2 4-bit memory
- Only one full-adder!
- 4 clocks to get the output (sequential adder)

---
Types of Sequential Circuits
- Synchronous
  - State changes synchronized by one or more clocks
  - Easier to design and analyze
- Asynchronous
  - Changes occur independently
  - Faster
  - Hard to design and analyze

---
Clocks in Synchronous Circuits

---
Basic Storage
- Apply low or high for longer than tpd
- Feedback will hold value

---
SR (set-reset) Latch
- Basic storage made from gates
- When S & R are both 0 → “keep” state
- When S & R are both 1 → undefined!

---
S'R' (set-reset) Latch
Similar – made from NANDs

---
Add Control Input
- Control when state can change
- How about the undefined state?

---
D-Latch
No undefined state

---
Transparency of latches
- As long as C (the control ) is high, state can change
  - This is called transparency
- Results are unpredictable
- Behavior depends on gate delays and not logical values

---
Flip-Flops (Solving Transparency)
- Flip-Flops:
  - Ensure output changes only once per clock cycle
- Two commonly-used types of flip-flops:
  - Master-Slave:
    - Use two latches
  - Edge-Triggered:
    - Implemented very different from latches
    - Triggers at signal transition (positive, negative)

---
SR Master-Slave Flip-Flop
- Two latches and an inverter
- Either Master or Slave is enabled, not both

---
Edge-Triggered Flip-Flops
- Changes at input of FF when clock high do trigger next state.
  - Is this a problem?
  - Master-Slave sometimes called pulse triggered
  - As clock goes faster, more problems
- New state latched on clock transition
- Low-to-high: positive-edge triggered
- High-to-low: negative-edge triggered
- Also: dual-edge-triggered

---
D-Type Edge-Triggered
Positive or negative?

---
Standard Symbols

---
Standard Symbols

---
Direct Inputs
- Force Set/Reset independent of clock
  - Direct set or preset
  - Direct reset or clear

---
Propagation Delay
The times it takes for an input to appear at the output is called the propagation delay.

---
Setup and Hold Times
- Setup time (Ts) refers to a constant duration for which the inputs must be held prior to the arrival of the clock transition
- Hold time (Th) refers to the duration for which the inputs must not change after the arrival of the transition

---
Design procedure

---
Question
- Design a circuit to detect a sequence of 3 ones (111) or more using D-FF. The circuit has one input X and one output Z.
  - Draw the state diagram
  - How many FF do you need? Why?
  - Derive the state table
  - Obtain the simplified equations
  - Draw the circuit

---
Assignment
Read experiment 1 in the lab manual