## Slide 1: Senior Project Discussion
Handicapped Parking Spots
Coordinator: Dr. Ahmad Khayyat
Supervisor: Dr. Kamal Chenaoua
Team Members: Mohammad Makkawi
Rami Rustom
Yazan Hlayel

## Slide 2: Outline
Introduction
  Background.
  Problem Statement.
  Marketing Requirements
Design and Architecture
  Logical Design
  Subsystems
  Design Decisions
  Technical Specifications
  Component and Interfacing
Implementation
  Sub-Systems Implementation
  Integration
  Issues
  Limitations
Conclusion

## Slide 3: Introduction
The Problem
  Handicapped parking abuse.
  Affects 72% of handicapped.
How big is it ?
  Many attempts to solve the problem.
  APPs to report abusers.
Why ?
  “I feel there are too many parking spaces reserved for the handicapped”
  “I feel many people who have handicapped parking license do not really need them”

## Slide 4: Current Solutions
Issue a handicapped permit from “The Ministry of Social Affairs”.
Guard to check the parked cars.
Remote controlled gates.

## Slide 5: Proposed Solution Requirements
Allow only eligible people to use the parking spot.
Show the number of empty handicapped spots at the entrance of the parking.
Ability to issue temporary permits to use handicapped spots.

## Slide 6: Design and Architecture

## Slide 7: Logical Design
Controller
Blocking
Counting
Car
Detector

## Slide 8: Subsystems
Identification
  Reader
  Tag
Blocking
  Controllable Gate
Counting
  Controller
  Screen

## Slide 9: Design Decisions
Identification sub-system
  License Plate Recognition
  Passive RFID
  Active RFID
  QR code
Blocking method
  Parking space guard
  Electro-Hydraulic Spike Barrier
  Electro-hydraulically Blocking Bollards
  Parking Post
Passive RFID
  Hard to forge (secure).
  Cheap.
  Easy to use.
  Has security (challenge and response).
Parking space guard
  Integrated radio receiver
  Handheld radio transmitter
  solar technology (outdoor)
  one way blocking (with sensors)

## Slide 10: Design Decisions
Controller
  Arduino
  Raspberry pi
  Atmel
Arduino
  Developer friendly
  Plenty of digital pins
  Availability in the market
  Accessories

## Slide 11: Technical Requirements
MAX 1KB Passive RFID tags issued for handicapped people.
The tag contains information about the user and expiration date.
RFID antenna with a range of ~6 meters.
Blocking arm to secure the spot.

## Slide 12: Component
Identification
  UHF RFID Reader
  UHF RFID Antenna
  UHF RFID Tag
Counting
  Arduino Mega 2560
  TFT Display Screen
Blocking
  Grove Relay
  The car radio antenna

## Slide 13: Interfacing
Reader to Tag
  RF signals
Reader to Arduino
  digital signal
Arduino to TFT Display
  8 digital signals
Arduino to Relay
  digital signal

## Slide 14: Implementation
  Sub-Systems Implementation
    Identification and Authentication
    Blocking
    Counting
  Integration
  Issues
  Limitations

## Slide 15: Identification
RFID
What is it ?
Uses
Terminology
  RSSI
  RAPID

## Slide 16: Identification
Events :
Tag Arrive
Tag Depart (3 s)
Tag Report

## Slide 17: Identification
Tag Arrive
  Authenticate Tag ID
  Authenticate Tag Expiration
    Value
    Signed Value
  Add to “Monitor” list.
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1 | Tag Signature (0x0000FFFF) |  |  |  | Tag is Local or Public (0000FFFF OR FFFF0000) |  |  | 
2 | Owner ID |  |  |  | Owner mobile number |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 | Long Value (Issue Time) |  |  |  |  |  |  | 
6 | Expiration Time (Signed) |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  | 
8 | Long Value for (Expiration Time) |  |  |  |  |  |  | 

## Slide 18: Identification
Tag Report
  If tag is inside “Monitor” list.
  Check the distance (RSSI)
  Insure the tag isn’t moving.
  Make decision (Open/ Close)

## Slide 19: Identification
UHF tag (865-928) MHz.
64 Bytes memory.
Works in high temperature.
Orientation-independent.
Works with/around metal.

## Slide 20: Identification
Chart: Values of RSSI on Different Orientations
 | -356.3 | -362.3 | -357.5 | -352.9 | -374.1 | -370.4 | -356.6 | -360.3 | -369.3 | -362.3 | -344 | -344.1 | -365.9 | -367.8 | -366.3 | -380.2 | -357.4 | -366.9 | -367.2 | -376 | -376.1 | -366.6 | -369.5 | -350.5 | -357.3 | -349.6 | -376.8 | -350.6 | -357.9 | -377
Chart: Values of RSSI on Different Orientations
 | -330.3 | -325.6 | -329 | -332.1 | -322.9 | -328.8 | -323.4 | -328.2 | -328.1 | -325.4 | -330.6 | -329 | -334.1 | -329.4 | -327.8 | -325.7 | -325.5 | -335.2 | -332.5 | -327 | -329.7 | -328.6 | -334.3 | -331.7 | -332.8 | -329.9 | -328.3 | -328.3 | -329.3 | -324.8
Testing Tags Orientation

## Slide 21: Identification
Testing Tags Orientation

## Slide 22: Identification
Chart: RSSI
Chart: RSSI after smoothing
 | -436 | -437.85 | -438.2 | -438.55 | -428.65 | -432 | -442.85 | -451.4 | -461.6 | -474 | -484.4 | -502 | -511.15 | -523.2 | -525.9 | -531.2 | -541.5 | -547.9 | -551.5 | -558.4 | -573.8 | -582.25 | -575.65 | -583.25 | -593.15 | -608.2 | -618.85 | -626.25 | -619.95 | -610.9 | -610.3 | -618.1 | -621.45 | -624.7
=AVERAGE(INDEX(A:A;1+20*(ROW()-ROW($B$1))):INDEX(A:A;20*(ROW()-ROW($B$1)+1)))

## Slide 23: Implementation
  Sub-Systems Implementation
    Identification and Authentication
    Blocking
    Counting
  Integration
  Issues
  Limitations

## Slide 24: Blocking system
Black
  Ground
Red
  12v
White
  Relay

## Slide 25: Counting system

## Slide 26: Control code
Include TFT display library
Define the TFT display pins
Define the TFT display
Define all the needed variables
setup{
  Define the pin modes for input and output
  Define the default value for each output pins
  current value (cv) = opposite the signal coming from the reader
  Write the initial value on the screen
}
loop class {
  Write the new value on the screen
  New value (nv) = signal coming from the reader
  If cv != nv {
    Check the coming signal twice with a 5s delay in between
    Close or open the gate based on the signal
    Refresh the counter
    Write the new value on the screen
    Cv = nv
  }
}

## Slide 27: System integration

## Slide 28: Issues
Running the code on the reader.
Digital I/O not working
Buying the blocking device
Building the blocking device
Choosing the representative device
Refreshing the text on the TFT screen

## Slide 29: Limitations
TFT screen library
the specifications of the RFID reader
digital I/O ports in the RFID reader
Numbers of supported antennas.

## Slide 30: Conclusion
Developing applications by utilizing RFID technologies.
Using Arduino with enterprise devices and tools.
Controlling high voltage devices with a low voltage signals using relays.
Using third-party libraries to perform specific tasks and enhance the output.